## Slide 1: Measuring Your Electricity Consumption

## Slide 2: Energy Inventory Questions:
Is the little stuff a bigger deal than the big stuff?
Annually, is your car or your home electricity use responsible for more CO2 emissions? Do you spend more money on electricity or gasoline?
Classify devices based on high/low power and high/low energy. Are there any surprises?
What are possible sources of “parasitic losses”? Are these a big deal?

## Slide 3: Procedure
Using a power meter, record the KW used by the equipment 6 times, once every 10 seconds.
Obtain the average of these readings.
Multiply the average by the number of hours you use the equipment every day to get kWh.

## Slide 4: Example: My Nightstand Lamp
Readings:
10 sec: 37.5 W
20 sec: 37.1 W
30 sec: 37.3 W
40 sec: 37.1 W
50 sec: 37.3 W
60 sec: 37.1 W
Average (ignore the highest and the lowest values to eliminate extremes): (37.1 + 37.3 + 37.1 + 37.3) / 4 = 37.2 W
Usage: 4 hours/day
Electricity: 37.2 * 4 / 1000 = 0.149 kWh/day
Figure from A-V Designs
Notes: http://www.a-v-designs.com/desk-lamps/

## Slide 5: Your turn

## Slide 6: Other Equipment You May Have
Electric Space Heater:
Off = 0 W
Low Setting = 631.5 W
Medium Setting = 915.5 W
High Setting = 1500 W
Air Conditioner:
Off = 0 W
On = 600 W
Cable Box:
Off = 20.65 W
On = 20.78 W
Mini Fridge:
Off = 0 W
On = 90 W
X-Box 360:
Off = 0 W
On = 100 W
PS II
Off = 0 W
On = 45 W
TV :
Off = 4.5 W
On = 55.75 W
DVD:
Off = 0 W
On = 11.6
←Parasitic Loss
Notes: X-Box:
Off = 0 W
On = 100 W
PS II
Off = 0 W
On = 45 W
TV :
Off = 4.5 W
On = 55.75 W
DVD:
Off = 0 W
On = 11.6

## Slide 7: So, how much electricity do you use in your room?

## Slide 8: Question 1
Is the little stuff a bigger deal than the big stuff?

## Slide 9: Question 2
Annually, is your car or your home electricity use responsible for more CO2 emissions? Do you spend more money on electricity or gasoline?

## Slide 10: Question 3
Classify devices based on high/low power and high/low energy. Are there any surprises?

## Slide 11: Question 4
What are possible sources of “parasitic losses”? Are these a big deal?

## Slide 12: World Electricity Consumption Totals (2004)

## Slide 13: World Electricity Consumption Per Capita (2004)